## Slide 1: PRESENTATION ON INDUSTRIAL ATTACHMENT
MEMBERS:
ADITYA AMATYA(072BME603)
NABIN NEUPANE(072BME623)
SANJEEB PAUDEL(072BME637)
UJWAL DHAKAL(072BME649)
TRIBHUWAN UNIVERSITY
INSTITUTE OF ENGINEERING
PULCHOWK CAMPUS

## Slide 2
OUTLINE OF THE PRESENTATION

## Slide 3
Background:
Dairy Development Corporation(DDC)
Established in 2026 B.S.
One of the leading dairy product manufacturer of the country
Nationwide coverage
Annual 60 million liters of milk collection

## Slide 4
Objectives of DDC:
To provide a guaranteed market for milk to the rural farmers with fair price.
To supply pasteurized milk and milk products to urban consumers.
To develop organized milk collection system to meet increasing demand for pasteurized milk and milk products.
To develop an organized marketing system for milk and milk products in urban areas.

## Slide 5
Flow Network:
Market
Processing Plants
Chilling Centers
Collection Centers
Farmers

## Slide 6
Objectives of Industrial Attachment:
To visit and work in different kinds of industries in the country

## Slide 7
Objectives of Industrial Attachment:
To study the existing management system and technology of that industry

## Slide 8
Organizational Structure:
Board of Directors
General Manager
Planning
Quality Control
Marketing Management
Management
Finance
Production Management
Internal Audit Section
Projects
Management
Technical
Technology Division
Sales
Marketing
Purchase
Internal Management
Human Resource
Computer Section
Training
Internal Audit Examination
Budget
Economic Analysis
Assets

## Slide 9
Plant Layout:
S.N. | Description | S.N. | Description | S.N. | Description
1 | Main Gate | 11 | Deep Freeze | 21 | Butter Production Room
2 | Guard House | 12 | Bike Stand | 22 | Milk Cold Storage
3 | Clinic | 13 | Ghee Section | 23 | Butter Cold Storage
4 | Changing Room and Toilet | 14 | Boiler Room | 24 | Butter Packing
5 | Bike stand | 15 | Power Control Room | 25 | Milk Production
6 | Oil Storage Tank | 16 | Total Store Room | 26 | Administration
7 | Guard House | 17 | Compressor Room | 27 | Garden
8 | Canteen | 18 | Workshop | 28 | Auto Workshop
9 | Water Treatment Plant | 19 | Engineering and Maintenance | 29 | Fresh Milk Unit
10 | Evaporator | 20 | Butter Cold Storage Room | 30 | Generator Section
9

## Slide 10
Products Manufactured From Kathmandu Milk Supply Scheme (KMSS):
Pasteurized Milk
Butter
Ghee
Flavored Milk
Curd

## Slide 11
Pasteurized Milk:
Milk Reception from chilling centers
Immediate Holding
Filling
Cooling/ Refrigeration
Distribution
Filtration and Cooling
Preheating to 400C
Cream Separation at 40-450C
Standardization
Homogenizer
Pasteurization at 760C/15sec
Cooling

## Slide 12
Butter:
Milk Reception from chilling centers
Distribution
Cream Separation (Centrifugal)
Cream
(35-50% fat)
Pasteurization
(82-880C, few sec)
Cooling (5-100C)
Churning
(9-110C, 45-75 min)
Check and Balance of Moisture Content
Packaging and Storage
(-10 to -200C )
Sampling
Testing

## Slide 13
Ghee:
Receiving Butter
Clarification
Storage in Tank
Filling at 450C
Ghee Melting VAT
Melting at 800C
Ghee Stratification
Holding
Draining
Boiling at 1100C
Filtration
Storage
Purchase of Plastic
Quality Control

## Slide 14
Flavored Milk:
Receiving Milk
Inspection
Sterilization at 1210C, 20 min
Storage
Distribution
Test (COB, Alcohol)
Cooling at 50C
Addition of sugar, color and flavor
Mixing by agitation
Transfer in Reservoir
Filling in Bottles
Crowning
Cooling at room temperature
Labeling
Recollecting Bottles
Dipping in Chemical Solution
Brushing
Store Facing Downwards
Inspection
Machine Cleaning

## Slide 15
Steam Production:
Boilers:
Fire Tube Boiler
Steam Distribution Center
Capacity: 2000 kg/hour
2-6.5 bar pressure
88% Efficient

## Slide 16
Steam Distribution Flow Diagram:

## Slide 17
Refrigeration System:
Cooling of Milk
Storage of Ghee and Butter
Pasteurization of milk and Cream
Needs of Refrigeration System:
Vapor Compression Refrigeration Cycle
Refrigerant Used:
R22 (Chlorodifluoromethane)
Ozone Depletion Potential (ODP)
Global Warming Potetial (GWP)

## Slide 18
Maintenance Crew:
Maintenance works are carried under production management section
Technical Engineers, foremen and workers are present for maintenance works

## Slide 19
Frequent need of Maintenance works:
Bearings and washers of RMC Packaging Machine
Pipes joints leaks
Compressor oil leakage
Conveyor Stoppage

## Slide 20
Breakdown Maintenance of Compressor:
Diagnosis:
Oil leakage due to misalignment of compressor shaft
Problem Statement:
Fast decrease in level of refrigerant in the system resulting in disrupted cooling of butter storage

## Slide 21
Breakdown Maintenance of Compressor:
Solution Adopted:
Replacement of the Compressor unit with a new one

## Slide 22
Task Assigned:
We were assigned to design a effective layout of the Conveyor system to carry packaged milk from packaging machines to the cold storage

## Slide 23
Necessity of the task:
There was no conveyor for moving the milk packaged by the RMC packaging machines to the cold storage
Man-pushed trolley of crates were being used

## Slide 24
Proposed Layout:
1
1
2
3
3
3
Cold Storage

## Slide 25
Solidworks Model:

## Slide 26
Experienced actual industrial environment
Were familiarized with the existing management system of the industry
Were familiarized with the technology of the industry

## Slide 27
Internship at one of the biggest dairy manufacturers of the nation was a matter of pride
Observation of real life working situations helped a lot in learning
Objectives of the industrial attachment were met

## Slide 28
S.N | References
1. | Caldwell, G. (2003). The Small-Scale Diary.NR Press.
2. | Goff, G.H. (2009). The Diary Science and Technology Book. Canada: Guleph University Press.
3. | Chandan, R.C, & Kilara, A. (2011). Dairy Ingredients and Food Processing. Kerala: Scott Press.
4. | Mahajan, M. (2014). Industrial Engineering and Production Management.
5. | http://www.indianboilers.com/oil-and-gas-fired-fully-wetback-boiler.php
6. | http://www.dairydev.com.np/list/Kathmandu-Milk-Supply-Scheme-(KMSS)/32/103/0